## Slide 1: Measuring accessibility and transport performance by road and rail in Europe's regions and territories
Hugo Poelman
DG Regional and Urban Policy
Analysis and Policy Conception Unit
hugo.poelman@ec.europa.eu
Beograd, 22 May 2019

## Slide 2: Policy context
EU Cohesion Policy
  The EU's main investment policy
  Targets all regions and cities
  Supporting job creation, business competitiveness, economic growth, sustainable development and the improvement of citizens' quality of life
  Covers 1/3 of the EU budget
Cohesion policy helps improving the regions' infrastructure

## Slide 3: Future policy objectives (2021-2027)
A smarter Europe: innovative and smart economic transformation
A greener, low-carbon Europe: energy transition, circular economy, climate change adaptation and risk management
A more connected Europe: mobility and ICT connectivity
A more social Europe: quality employment, education, skills, social inclusion and equal access to healthcare
A Europe closer to citizens: sustainable development of urban areas and other territories

## Slide 4: Specific role of the Funds
European Regional Development Fund (ERDF)
  Focus of spending in areas crucial for jobs and growth: smarter Europe and greener, low-carbon Europe
Cohesion Fund
  Investment in areas of environment, low-carbon economy and mobility
Special focus on (local) urban development (proposal: 6% of ERDF budget)

## Slide 5: Assessing investment needs
Each of the objectives translates in regional/territorial investment needs, to be monitored by comparable statistics
European statistical system delivers adequate sub-national data in various domains
Environmental reporting adds sub-national information
Geospatial data and analysis helps filling the data gaps, for instance in areas like mobility, access to health care or education

## Slide 6: The role of geospatial data and analysis
Identify thematic areas where data can be enhanced
Develop methodologies producing indicators
Demonstrate the feasibility of indicator production by using the available geospatial data
Identify gaps in data availability and promote a strategy towards a better provision of the required geodata

## Slide 7: Towards a framework of indicators on transport performance
Accessibility and performant transport networks and services are key factors for regional and territorial competitiveness
Indicator framework informing about:
  Infrastructure endowment
  Network characteristics
  Availability of transport services
  Accessibility provided by network and services
  Performance of the network and the services
Framework usable at various territorial levels

## Slide 8: Accessibility by road and by rail
How do regions/territories/cities perform in terms of road and rail accessibility?
Assess daily accessibility to (residential) population
Using a method designed to produce indicators at a wide variety of territorial levels
Basic units of analysis: 1 km² grid cells
Combination of GEOSTAT population grid, a complete road network and passenger rail timetables

## Slide 9: Road accessibility and transport performance
Creation of an accessibility area of 1h30 around each of the 2 million populated grid cells
Accessible population = sum of population living in that area
Transport performance: accessible population divided by population living in an area of 120 km radius around the departure grid cell x 100
  Accessibility taking into account the population distribution in the surroundings of the place of departure

## Slide 12: Spatial aggregations
From grid cells to
  Cities, urban centres, functional urban areas,…
  NUTS regions
  Degree of urbanisation
Population-weighted average accessibility and transport performance:
  Average accessibility or transport performance, starting from all populated grid cells located in the city / region / territory
  Weighted by the population of the grid cell of origin

## Slide 13
Transport performance by car by refined* degree of urbanisation
* distinguishing
- towns and suburbs
- villages, dispersed rural areas and mostly
uninhabited areas

## Slide 15: Rail accessibility: problem statement
Accessibility varies according to the day and time of travel
Comprehensive timetables and location of stations needed
Daily accessibility: focus on services at peak hours of an ordinary weekday
Manage vast amount of travel time calculations
Model the relationship between:
  travel time from station to station and
  the distribution of (grid) population

## Slide 16: Rail accessibility: computing travel time
  Travel times during peak hours
    Morning and evening peak periods on a weekday in 2014, each period 2 hours long
    We request travel times for each quarter of an hour; i.e. in total we run 18 requests for each pair of origin/destination stations
  For each pair of stations:
    The optimal travel time: the shortest travel time available, without any waiting
    The average total travel time: including the initial waiting time before first boarding; reflects the frequency of the available services

## Slide 17
Accessible stations = reachable within 1h30

## Slide 18: From stations to grid cells
All travel times are capped to 1h30
For each grid cell close to a departure station we compute the population of all grid cells close to all stations that can be reached within 1h30
"Close to a station" = within short walking or cycling distance
rail +
walking
rail +
cycling

## Slide 19
Average travel time, combined
with a short walk
Optimal travel time, combined
with a short bike ride
Transport performance by rail plus a short walk (or bike ride)

## Slide 21: Transport performance and infrastructure endowment

## Slide 22: Transport performance and population concentration

## Slide 23: Results
Grid level combined with comprehensive road and rail data ensures maximum flexibility of output
Variety of regional and territorial accessibility patterns helps characterising different challenges the regions are facing
  Infrastructure needs (bottlenecks, missing links,…)
  Spatial distribution of population; urban sprawl challenge
  Adequate provision of public transport services
  Improving opportunities for active mobility modes
All results will be described in a forthcoming Working Paper

## Slide 24: Future opportunities
Opportunities (and challenges…)
  More frequent grid data
  Towards grid of daytime population; employment??
  Future use of complete and authoritative road and rail networks?
  Open and standardised up-to-date rail timetable data
  Ongoing development of routing software to enhance the computational possibilities (e.g. increase temporal resolution)

## Slide 25: Conclusion
Combinations of currently available geospatial data provide very interesting opportunities for indicator development, thanks to the efforts of many stakeholders
Further developments and mainstreaming will require
  Better harmonisation of (open) data from authoritative sources
  More data on the location of (public) services
  Improved completeness and timeliness
  Data fit for analytical purposes (e.g. routing)
  Future development of grid-based statistics